## Slide 1: Lattice Slides

## Slide 2: Contract Problem Statement
Define a contract between the LEC sensor and CPS controller
  Contract: A pair of properties, one for the LEC and one for the CPS
  If both the LEC and the CPS controller satisfy the contract, then the overall system is safe
  Allows for separate analysis of the LEC and CPS
Notes: Where does the lattice fit into this whole problem setup?
Contracts: Some sort of assume guarantee type argument
Anlayze controller to determine what the LEC needs to guarantee for safety
Analyze the LEC to determine if it meets this property
Or vice versa
Deriving what these contracts should be is quite tricky
There’s no existing procedure to do this
There are also tradeoffs between contract simplicity and underapproximating safety
EG simple contracts will be easy to analyze, but may give poor safety results
And complex contracts will give better safety results, but will be more difficult to analyze
Our current approaches for creating these contracts include
Analyzing safe controller traces to determine what ‘safe LEC traces’ look like
gives us our K and N style contracts
These contracts are difficult to derive, since they require enumerating large sets of controller traces
So we need more ways of creating these contracts
One potential solution: lattice
Compute the system dynamics as a function of LEC readings (or sequences of LEC readings)
The lattice is discrete to ensure the analyzing it remains tractable
tradeoff between complexity and safety
The lattice itself becomes a contract
The controller builds the lattice
The LEC gives the probability that it can reach unsafe parts of the lattice
- Using some probabilistic abstraction of the LEC

## Slide 3: Deriving/Creating Contracts
These contracts are difficult to derive
  They can take many forms
Our current work has focused on deriving safe sequences of LEC outputs from safe sequences of controller outputs
  Difficult to get high probability sequences
    Need to generate a lot of sequences
  Tricky to keep these analyses strictly ‘worst case’
    Especially when there are multiple controller regions
We are looking at using the lattice to generate contracts

## Slide 4: Lattice Contract
The controller creates the lattice and computes the lattice transitions as a function of the LEC readings
  Use a discrete lattice to ensure the analyses remain tractable
  The lattice and its associated transitions are the contract
  Mark which lattice points are unsafe
The LEC gives the probability that it can reach the unsafe parts of the lattice
  Using some probabilistic abstraction of the LEC
  This analysis can be done in PRISM
If the lattice analysis is intractable on the LEC side, then the controller can reduce the granularity of the lattice to simply the LEC analysis
  Allows for the contract to be iteratively refined
Notes: So we need more ways of creating these contracts
One potential solution: lattice
Compute the system dynamics as a function of LEC readings (or sequences of LEC readings)
The lattice is discrete to ensure the analyzing it remains tractable
tradeoff between complexity and safety
The LEC gives the probability that it can reach unsafe parts of the lattice
- Using some probabilistic abstraction of the LEC

## Slide 5: Lattice Update
Last time we talked about how a single pair of K and N values can lead to multiple transitions on the lattice
  Due to the ordering of LEC detections and misdetections
To address this issue, we will allow for these nondeterministic transitions on the lattice
  Use an MDP solver to compute the worst-case probability of safety
    Eg PRISM

## Slide 6
Distance (m)
Velocity (m/s)
K=2
K=2
N=5